## Slide 1
NETWORK TOPOLOGIES
Understanding how computers are physically & logically connected: Bus, Star & Tree Topologies
PRESENTER NAME
Devesh
CLASS & SECTION
Class 12 - A
ROLL NUMBER
17

## Slide 2
Key Networking Concepts & Terms
A unique 12-digit hexadecimal physical address (NIC card) burned into hardware to identify devices on a local network.
Hardware devices placed at both ends of a Bus cable to absorb electrical signals and prevent signal reflection (bounce).
The primary high-capacity transmission cable that carries data traffic between network branches or workstations.
The central connection box in Star topologies that receives packets and directs them toward destination nodes.
Any active device attached to a network (computer, printer, server) capable of sending or receiving data.
Formatted units of digital data transmitted across a network, containing source MAC, target MAC, and payload.
MAC Address
Terminators
Backbone Cable
Central Switch / Hub
Node / Workstation
Data Packet

## Slide 3
CONCEPTS
What is a Computer Network?
Core Definition
An interconnected collection of autonomous computers capable of exchanging data, sharing software, and accessing centralized hardware.
Data Sharing
Instant digital file transfers across workstations.
Hardware Sharing
Shared central printers, storage drives, and servers.
Communication
High-speed messaging and effective information exchange.
QUESTION
Can two standalone computers share a printer without forming a network?

## Slide 4
DEFINITION
What is Network Topology?
Network Topology refers to the geometric arrangement of nodes, interconnecting cables, and networking devices in a system.
The physical placement of cables, computers, patch panels, and switches placed across the floor or building.
The path that electronic signals take to travel across nodes regardless of physical device layout.
1. Physical Topology
2. Logical Topology

## Slide 5
The 3 Core Network Topologies
Bus Topology
Single Backbone Cable
All computers connect to one continuous central communication line with terminators at both ends.
Star Topology
Central Switch / Hub
All computers connect independently to a single central network switch or hub.
Tree Topology
Hierarchical Branches
Combines Star clusters connected together along a main central backbone trunk.
TOPOLOGY 01
TOPOLOGY 02
TOPOLOGY 03

## Slide 6
KEY: TERMINATOR
Note: Terminators absorb electrical signals at cable ends to prevent signal reflection.
SINGLE BACKBONE CABLE
Bus Topology — Structure & Working
WORKING MECHANISM
1. Broadcast Signal: Sender transmits data along the backbone cable. 2. Address Verification: Nodes inspect target MAC address. 3. Signal Absorption: Terminators absorb signals at cable ends.
PROS
• Minimum cable required. • Low setup cost for small labs.
CONS
• Backbone break fails network. • Collisions under heavy traffic.

## Slide 7
KEY: CENTRAL SWITCH
Real Lab Standard: Most school computer labs deploy Star Topology for easy troubleshooting.
CENTRALIZED CONTROL UNIT
Star Topology — Structure & Working
WORKING MECHANISM
1. Point-to-Point Link: PC sends packet directly to central Switch. 2. Address Switching: Switch reads MAC address and routes directly. 3. Fault Isolation: Cable failure on 1 PC doesn't affect rest.
PROS
• Easy fault detection. • 1 PC failure won't stop lab.
CONS
• Switch failure downs whole lab. • Higher cabling cost.

## Slide 8
KEY: STAR + BUS TRUNK
Note: Tree Topology = Bus Topology + Star Topology (Star clusters connected along a central backbone).
HIERARCHICAL BRANCHES
Tree Topology — Structure & Working
WORKING MECHANISM
1. Local Cluster Routing: Intra-building traffic stays in local switch. 2. Inter-Branch Trunking: External data passes up central trunk. 3. Tiered Scalability: New Star clusters easily attach to trunk line.
PROS
• Highly scalable for campuses. • Isolates faults by branch.
CONS
• High cable & device cost. • Main trunk failure disconnects branches.

## Slide 9
Feature | Bus Topology | Star Topology | Tree Topology
Central Core | Single Cable | Switch / Hub | Hierarchical Trunk
Cable Cost | Lowest Cost | Moderate Cost | High Cost
Fault Impact | Cable break downs all | Only 1 PC affected | Branch isolated
Ideal Use Case | Small office / Home | School Computer Lab | Multi-building Campus
Direct Comparison: Bus vs Star vs Tree

## Slide 10
Some Important Questions:-
STAR TOPOLOGY
TERMINATORS
TREE TOPOLOGY
Q1: Which topology connects all workstations to a central Switch/Hub?
Q2: What hardware prevents signal bounce in a Bus topology?
Q3: Which topology is best for a large multi-building school campus?

## Slide 11
Summary
Bus Topology
Single backbone cable. Best for low budget small setups.
Star Topology
Central Switch. Standard for school computer labs.
Tree Topology
Hierarchical combo. Ideal for large campus networks.
Thank You!
Any questions or discussion points from the teacher or classmates?